## Slide 1: Stream Floating: Enabling Proactive and Decentralized Cache Optimizations
Zhengrong Wang1, Jian Weng1, Jason Lowe-Power2,
Jayesh Gaur3, Tony Nowatzki1
1UCLA, 2UC Davis, 3Intel
Feb. 2021

## Slide 2: Information Gap Reactive Cache System
Reactive Cache System:
72% cached lines without reuse.
Up to 30% extra control NoC traffic.
Missing holistic view of the program behavior.
Notes: Cache system has been dealing with the information gap for decades.
It has taken many approaches to solve this problem: prefetchers, reuse policy.
Von-Neumann
Specialization has been a huge success for computation. This can also been applied to memory.

## Slide 3: Streams to Bridge the Gap Proactive Cache
Proactive Cache System:
Driven by streams, proactively transfer.
Notes: Cache system has been dealing with the information gap for decades.
It has taken many approaches to solve this problem: prefetchers, reuse policy.
Von-Neumann
Specialization has been a huge success for computation. This can also been applied to memory.

## Slide 4: Stream Floating Proactive Cache System

## Slide 5: Stream Floating Implementation
Configure
Usage
Advance
Original C Code
int i = 0;
while (i < N) {
sum += B[A[i]];
i++;
}
Stream Pseudo-Code
stream_cfg(B[A[]]);
while (i < N) {
sum += stream_ld();
stream_step();
}
Static + dynamic information floating decision.
e.g. reuse distance, aliased stores, hit rate in L2.
Offload entire stream pattern with one message.
Proactively transfer stream data.
Stream data is not cached (bypass coherence).
Extend MESI with GetUncached request.
Automatically migrate to next bank.
Keep streaming until no credits.
Released by StreamEnd message.
Weak consistency w. aliasing detection.
Strong consistency is also possible.
w. stream-grain coherence.
Indirect requests from remote SEL3.
Decentralized address generation.

## Slide 6: NoC Traffic Breakdown
Chart: Travelled Hops
| conv3D | mv | bfs | hotspot | nw | particlefilter | pathfinder | avg.
Base | 0.29045 | 0.39898 | 0.41383 | 0.40219 | 0.38023 | 0.25164 | 0.37839 | 0.36276
Base | 0.70955 | 0.60102 | 0.58617 | 0.59781 | 0.61977 | 0.74836 | 0.62161 | 0.63724
Base | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
L1BG-L2ST | 0.44157 | 0.40442 | 1.0518 | 0.47088 | 0.71157 | 0.25686 | 0.41567 | 0.49957
L1BG-L2ST | 0.99432 | 0.6089 | 1.4423 | 0.71545 | 1.0818 | 0.76084 | 0.67085 | 0.84009
L1BG-L2ST | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
SF-Aff | 0.054829 | 0.011099 | 0.36614 | 0.2342 | 0.19883 | 0.0045303 | 0.077951 | 0.15045
SF-Aff | 0.52669 | 0.49574 | 0.59921 | 0.44448 | 0.56215 | 0.74481 | 0.2784 | 0.53214
SF-Aff | 0.032382 | 0.020251 | 0.042899 | 0.01073 | 0.034123 | 0.037364 | 0.0092942 | 0.020343
SF-Ind | 0.054375 | 0.0117 | 0.3682 | 0.23416 | 0.19868 | 0.0045244 | 0.077955 | 0.15067
SF-Ind | 0.52607 | 0.49633 | 0.49913 | 0.4444 | 0.5621 | 0.74481 | 0.27842 | 0.52544
SF-Ind | 0.032381 | 0.020251 | 0.03962 | 0.010728 | 0.034119 | 0.037361 | 0.009293 | 0.020063
2.49
1.79
1.42
1.33
Control
Data
Stream
1.39 speedup over hardware prefetcher.
36% NoC traffic reduction.
L1BG-L2ST: L1 Bingo spatial + L2 stride prefetcher.
Baseline: No HW prefetcher or stream support.
SF-X: Stream-floating with each optimization enabled.

## Slide 7: Conclusion: Streams Enables Proactive Cache
Proactive Cache System:
Driven by streams, proactively transfer.
Explore rich ISA semantics in the cache system.

## Slide 8: Stream Floating: Enabling Proactive and Decentralized Cache Optimizations
Zhengrong Wang1, Jian Weng1, Jason Lowe-Power2,
Jayesh Gaur3, Tony Nowatzki1
1UCLA, 2UC Davis, 3Intel
Feb. 2021

## Slide 9: Information Gap Reactive Cache System
Reactive Cache System:
72% cached lines without reuse.
Up to 30% extra control NoC traffic.
Missing holistic view of the program behavior.
Notes: Cache system has been dealing with the information gap for decades.
It has taken many approaches to solve this problem: prefetchers, reuse policy.
Von-Neumann
Specialization has been a huge success for computation. This can also been applied to memory.

## Slide 10: Streams to Bridge the Gap Proactive Cache
Proactive Cache System:
Driven by streams, proactively transfer.
Notes: Cache system has been dealing with the information gap for decades.
It has taken many approaches to solve this problem: prefetchers, reuse policy.
Von-Neumann
Specialization has been a huge success for computation. This can also been applied to memory.

## Slide 11: Stream Floating Proactive Cache
Expose stream patterns without reuse to shared L3 banks.
Proactive cache system that driven by streams.
  One request for an entire stream.
  Accurate prefetch.
  Simplified coherence protocol.
1.39 speedup over hardware prefetcher.
36% NoC traffic reduction.
Notes: Cache system has been dealing with the information gap for decades.
It has taken many approaches to solve this problem: prefetchers, reuse policy.
Von-Neumann
Specialization has been a huge success for computation. This can also been applied to memory.

## Slide 12: Outline
Insights and Opportunities
Stream Floating Implementation
Coherence and Consistency
Evaluation

## Slide 13: Outline
Insights and Opportunities
Stream Floating Implementation
Coherence and Consistency
Evaluation

## Slide 14: Overheads of Caching Data without Reuse
Chart: L2 Eviction
| conv3D | mv | bfs | b+tree | cfd | hotspot | hotspot3D | nn | nw | particlefilter | pathfinder | srad | avg.
NoReuse | 0.81008 | 0.99219 | 0.55399 | 0.85643 | 0.71267 | 0.53173 | 0.79559 | 0.85127 | 0.52348 | 0.9956 | 0.57495 | 0.44172 | 0.71997
NoReuse-Stream | 0.78277 | 0.95101 | 0.50808 | 0.72012 | 0.68477 | 0.23241 | 0.78749 | 0.76976 | 0.4548 | 0.98849 | 0.50665 | 0.14331 | 0.62747
Chart: Flits Injected
| conv3D | mv | bfs | b+tree | cfd | hotspot | hotspot3D | nn | nw | particlefilter | pathfinder | srad | avg.
NoReuse-Ctrl | 0.1389 | 0.33417 | 0.16277 | 0.18953 | 0.23475 | 0.19922 | 0.26214 | 0.17568 | 0.16383 | 0.24417 | 0.18225 | 0.15397 | 0.20345
NoReuse-Data | 0.39353 | 0.38606 | 0.26175 | 0.3471 | 0.26465 | 0.20037 | 0.3103 | 0.17644 | 0.16453 | 0.72984 | 0.18366 | 0.1541 | 0.2977

## Slide 15: Conventional vs. Stream Floating

## Slide 16: Outline
Insights and Opportunities
Stream Floating Implementation
  What to offload?
  How to offload?
  When to offload?
Coherence and Consistency
Evaluation

## Slide 17: What to Offload: Streams
Stream: A decoupled sequence of values/addresses [ISCA’ 19].
Explicitly embedded in the ISA.
Memory order defined by the first usage of the value.

## Slide 18: Stream Engines
SECORE:
Mange stream configuration and issue stream requests.
Make and cancel offload decisions.
SEL2:
Buffer stream data and match it with requests from SECORE.
Issue flow control credits to remote L3 bank (SEL3).
SEL3:
Generate requests and stream back data to SEL2.
Receives control messages from SEL2, e.g. flow credits.
SECORE

## Slide 19: How to Offload: Configure Affine Stream A[i]
SECORE configures SEL2 with the affine stream pattern A[i].
SEL2 allocates the stream buffer, and forward configuration to SEL3 where A[0] is.

## Slide 20: How to Offload: Proactively Stream Data to Core
SEL3 generates requests of A[i], translates (L2 TLB) and sends to L3 cache controller.
Data responses are buffered at SEL2 and later drained by requests from SECORE.

## Slide 21: How to Offload: Flow Control and Migration
SEL2 sends out credits to SEL3 at coarse-granularity, further reduce traffic overhead.
Streams migrate to the next bank, and keep streaming until no credits.
Slightly increase interleave granularity to avoid too-frequent migrations.

## Slide 22: How to Offload: End (Sink) the Stream
SECORE terminates streams by sending out StreamEnd messages.
SEL3 can directly release streams with known length.
Single Request – Multiple Data
Minimal control traffic for floating streams.
Deep and accurate prefetching.

## Slide 23: How to Offload: Indirect Stream B[A[i]]
Associate indirect stream B[A[i]] with A[i].
SEL3 can directly send out indirect requests to the target L3 cache controller.
Decentralized Address Generation
Generate indirect request at remote L3.
Only transfer the required subline data.

## Slide 24: How to Offload: Stream Confluence
Neighboring cores may be requesting the same piece of data.
SEL3 can easily perform pattern matching and multicast data to different cores.
Stream Confluence
Coordination between cores’ accesses.
Avoid duplicate data traffic.

## Slide 25: When to Offload: Detect Floating Candidates
Target: Streams with no reuse in the private cache, or aliasing.
Static Information: Compiler Analysis.
  E.g. are there writes to the address?
Dynamic Information: Stream History Table.
Only offload when passed both static & dynamic check.
  SECORE can early terminate a floating stream, e.g. found aliasing.

## Slide 26: Outline
Insights and Opportunities
Stream Floating Implementation
Coherence and Consistency
  Support Weak Consistency
  Support Strong Consistency
Evaluation

## Slide 27: Support Weak Consistency: Uncached Stream Data
Limit streams in synchronization-free region.
Bypass coherence protocol: stream data is not cached.
  Extend MESI protocol with uncached requests (GetU).
Details about aliasing detection in the paper.
Strong consistency with stream-grain coherence.
I à EE
I à I
I à E

## Slide 28: Outline
Insights and Opportunities
Stream Floating Implementation
Coherence and Consistency
Evaluation

## Slide 29: Configurations
LLVM-based compiler to recognize streams and transform programs.
Gem5 20.0 cycle-level execution-driven simulator.
12 data processing workloads from Rodinia and micro kernels.
  Parallelized with OpenMP, with AVX-512 enabled.
Configurations (see paper for details):
  8x8 mesh topology, 3-level MESI, 32kB L1 I/D, 256kB L2, 1MB L3.
  Base: Baseline cores without prefetcher or stream support.
  L1Stride-L2Stride: Stride prefetcher at both L1 and L2 cache level.
  L1Bingo-L2Stride: Bingo spatial prefetcher at L1 and stride prefetcher at L2.
  SS: Stream-specialized processor (stream support at core) [ISCA’ 19].
  SF: Stream floating, (offload stream to cache) [this work].

## Slide 30: Overall Speedup with IO4 and OOO8
Chart: Speedup
| conv3D | mv | bfs | hotspot | nn | nw | particlefilter | srad | geomean. | conv3D | mv | bfs | hotspot | nn | nw | particlefilter | srad | geomean. | IO4 | OOO8
Base | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
L1Stride-L2Stride | 2.4911 | 6.5642 | 1.2043 | 2.0706 | 1.5987 | 1.0187 | 2.4329 | 1.6535 | 1.9522 | 1.5069 | 2.2183 | 1.0998 | 1.6939 | 1.0418 | 1.0302 | 2.0088 | 1.9897 | 1.5933
L1Bingo-L2Stride | 3.3147 | 6.0699 | 1.1675 | 2.4149 | 1.6282 | 1.2068 | 2.8302 | 1.8663 | 2.1054 | 3.0081 | 2.2127 | 0.96499 | 1.5864 | 1.1004 | 1.2221 | 2.1823 | 2.1388 | 1.6801
SS | 3.6432 | 3.6691 | 1.7634 | 2.3353 | 1.4029 | 1.163 | 1.151 | 1.896 | 1.9509 | 2.6007 | 1.7572 | 1.0797 | 1.8106 | 0.99979 | 1.9016 | 2.3051 | 2.1515 | 1.7793
SF | 4.7994 | 8.496 | 2.221 | 4.2484 | 1.5092 | 1.7267 | 3.4128 | 1.9596 | 3.1966 | 3.951 | 3.2615 | 1.1267 | 2.2758 | 1.0727 | 2.0564 | 2.3249 | 2.3519 | 2.3396

## Slide 31: LLC Request Breakdown
Chart: Requests to L3 Cache
| conv3D | mv | bfs | b+tree | cfd | hotspot | hotspot3D | nn | nw | particlefilter | pathfinder | srad | avg.
Core-Normal | 0.0087387 | 0.0038855 | 0.28442 | 0.062746 | 0.085074 | 0.10507 | 0.0017979 | 0.0090833 | 0.056079 | 0.017152 | 0.090551 | 0.076059 | 0.066722
Core-Stream | 0.28594 | 5.6235e-05 | 0.1452 | 0.044183 | 0.5656 | 0.36192 | 0.22533 | 0.12764 | 0.43273 | 0.0058813 | 0.16676 | 0.70811 | 0.25578
Float-Affine | 0.19992 | 0.93874 | 0.12671 | 0.89244 | 0.24663 | 0.53301 | 0.64353 | 0.86327 | 0.51119 | 0.15434 | 0.74269 | 0.21583 | 0.50569
Float-Indirect | 0 | 0 | 0.44366 | 0 | 0.1027 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.04553
Float-Confluence | 0.50541 | 0.057317 | 0 | 0.00063455 | 0 | 0 | 0.12935 | 0 | 0 | 0.82263 | 0 | 0 | 0.12628

## Slide 32: NoC Traffic Breakdown
Chart: Travelled Hops
| conv3D | mv | bfs | hotspot | nw | particlefilter | pathfinder | avg.
Base | 0.29045 | 0.39898 | 0.41383 | 0.40219 | 0.38023 | 0.25164 | 0.37839 | 0.36276
Base | 0.70955 | 0.60102 | 0.58617 | 0.59781 | 0.61977 | 0.74836 | 0.62161 | 0.63724
Base | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
L1BG-L2ST | 0.44157 | 0.40442 | 1.0518 | 0.47088 | 0.71157 | 0.25686 | 0.41567 | 0.49957
L1BG-L2ST | 0.99432 | 0.6089 | 1.4423 | 0.71545 | 1.0818 | 0.76084 | 0.67085 | 0.84009
L1BG-L2ST | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
SS | 0.28892 | 0.39872 | 0.40962 | 0.40848 | 0.37624 | 0.25225 | 0.38067 | 0.36627
SS | 0.70633 | 0.59997 | 0.57983 | 0.60236 | 0.61419 | 0.74883 | 0.62556 | 0.63701
SS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
SF-Aff | 0.054829 | 0.011099 | 0.36614 | 0.2342 | 0.19883 | 0.0045303 | 0.077951 | 0.15045
SF-Aff | 0.52669 | 0.49574 | 0.59921 | 0.44448 | 0.56215 | 0.74481 | 0.2784 | 0.53214
SF-Aff | 0.032382 | 0.020251 | 0.042899 | 0.01073 | 0.034123 | 0.037364 | 0.0092942 | 0.020343
2.49
1.79
1.42
1.33
Control
Data
Stream

## Slide 33: Energy vs. Speedup

## Slide 34: Conclusion: Streams Enables Proactive Cache
Proactive Cache System:
Driven by streams, proactively transfer.
Explore rich ISA semantics in the cache system.